Sending AT commands to mobiles through minicom

1.1	Setup in Mobile
In settings press build number option 7 times then developer mode is on.then enable the usb debugging.connect mobile via data cable to linux PC.Once the device is connected, observe the output of dmesg for usb port path.
 EX: cdc_acm 1-5:1.1: ttyACM0: USB ACM device

### 1.2 Installing minicom
### In-order to send AT commands to modems, we need an interface. Minicom is a tool which provides an interface for communicating with devices that are connected to serial ports.
# apt-get install minicom

### 1.3 Configure minicom
       To configure minicom to access modem, do the following:
  # minicom -s
        +-----[configuration]------+
    | Filenames and paths |
        | File transfer protocols |
        | Serial port setup |
        | Modem and dialing |
        | Screen and keyboard |
        | Save setup as dfl |
        | Save setup as.. |
        | Exit |
        | Exit from Minicom |
        +--------------------+

Choose the “Serial port setup” and press “Enter”. It will display a screen similar to the following.
  +-----------------------------------------------------------------------+
    | A - Serial Device : /dev/ttyACM0 |
    | B - Lockfile Location : /var/lock |
    | C - Callin Program : |
    | D - Callout Program : |
    | E - Bps/Par/Bits : 115200 8N1 |
    | F - Hardware Flow Control : No |
    | G - Software Flow Control : No |
    | |
    | Change which setting? |
    +-----------------------------------------------------------------------+
Press ‘A’ to change the serial device from give the path that you find in dmesg.
Press ‘E’ to change the Baud rate at which the modem communicates.
Once you change these settings, press “Enter”.
Choose “Save setup as dfl” and choose “Exit”.
Now we have configured the minicom successfully and you will see a screen like the following.
Welcome to minicom 2.6.1
OPTIONS: I18n
Compiled on Feb 11 2012, 18:12:55.
Port /dev/ttyACM0
Press CTRL-A Z for help on special keys

1.4	AT commands
Press ctrl+A ,E to type AT commands
To test whether we have configured minicom successfully to communicate with modem, type “AT” in the minicom. You should get a “OK” response.
### 1. Answer an Incoming call – ATA
To answer an Incoming call via modem, issue the “ATA” command in the minicom.
RING
ATA
OK
When there is an incoming call, you can see a ‘RING’ message in the minicom. You can press “ATA” to answer the incoming call.
### 2. Dialing out and hanging up a voice call – ATD – ATH
You can also dial out a voice call from the modem using ATD command.
ATD 99769XXXXX;
OK
Now the phone will dial out to the number 99769XXXXX.
To hangup the call, use ATH command.
### 3. Getting the Manufacture/IMEI/IMSI information
Extended AT commands are used to provide information about the manufacturer, International Mobile Equipment Identity, International Mobile Subscriber Identity etc…
AT+CGMI
Nokia
OK
AT+CGSN
xxxxxxxxxxxxxxx
OK
AT+CIMI
xxxxxxxxxxxxxxx
OK
### 4. Getting Signal quality and battery charge status
You can also get the signal quality and the battery charge status using AT extended commands.
AT+CSQ
+CSQ: 29,99
OK
AT+CBC
+CBC: 1,96
OK
The output format +CSQ: 29,99 represents <Received signal strength indicator>,<Bit Error Rate>
The output format +CBC: 1,96 represents <current charging status>,<charged %>
### 5. Sending SMS using AT commands
You can also send SMS via AT commands.
AT+CMGF=1
OK
AT+CSCS=”GSM”
AT+CMGS="99xxxxxxxx"
> This is a test message
>
OK
The command AT+CMGF=1 sets the “Message format” to “text mode”. The command AT+CMGS, send the SMS to the specified number. < ctrl +z > is used to terminate the message input.
Press ctrl+A,Z to exit from minicom.

Refer the below links for more AT commands
https://www.developershome.com/sms/atCommandsIntro.asp